## Slide 1: Interrupt Mechanisms

## Slide 2: Module Syllabus
General Principles of Processor Interruption Techniques
Cortex-M0 Exception Types
Design and Implementation of an Interrupt Mechanism
  Integration with Timer
  Integration with UART

## Slide 3: Building a System on a Chip (SoC)
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-Segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral Drivers
AHB
Interrupt
Notes: This modules explores how to design and implement an interrupt mechanism that responds to interrupts from the timer and UART.

## Slide 4: Polling v Interrupts
How to display a number counting up every second:
Polling
  Use software to check if the hardware timer reaches a value.
  Slow: need to explicitly check to see if the timer has reached a value
  Wasteful of CPU time: the faster a response we need, the more often we need to check.
  Scales badly: difficult to build system with many activities that can respond quickly. Response time depends on all other processing.
Interrupt
  The timer generates an interrupt every second, and the processor runs specific code (interrupt service routine: ISR) in response.
  Fast: hardware mechanism
  Efficient: code runs only when necessary.
  Scales well
  ISR response time does not depend on most other processing.
  Code modules can be developed independently.
Notes: Let’s consider two fundamental types of processing structures: polling and interrupts.
In polling, program execution will be halted when an I/O operation is required. After that, the processor will keep checking the status of the I/O until it is ready. This approach wastes a great deal of CPU time; for example, if we are using this processing structure to display a number counting up every second, the software will need to repeatedly check the value held in the hardware timer to check when it reaches the value. This processing approach is not suitable for complex applications, as it is difficult to a build system with many activities which can respond quickly because response time depends on all other processing.
With interrupts, the hardware device being controlled, e.g., a UART peripheral, will cause a hardware interrupt to occur whenever it needs to be serviced, at which point the processor can interrupt the service routine. For example, if we are using this processing structure to display a number counting up every second, we can configure the timer peripheral to generate an interrupt every second, and the processor runs specific code (interrupt service routine: ISR) in response to display the number on a monitor or other display device. The interrupt driven approach is more efficient, as the code runs only when necessary. It is also fast as ISR response time does not depend on most other processing. In addition to this, the code modules can be developed independently.
This approach is particularly useful in low power applications, as the processor can enter sleep mode when no processing is required.

## Slide 5: Exception and Interruption
Exception
  Exceptions are events (internal or external) that cause the program flow to exit the current program thread and execute a piece of code associated with the event
  Events can be either internal or external.
  Exception Handler is a piece of software code that is executed in the exception mode.
Thread
Mode
Exception
Mode
Internal or external event
Executing exception
handler
Executing normal code sequence
Finishing handler
Context saving
Context restoring
Notes: In an interrupt-driven processing environment, we can differentiate between two types of interruption events: internal or external. Both cause the program flow to exit the current program thread and execute a piece of code associated with the event. An external event is called an exception handler. When the processor finishes executing the exception handler, it will return to the interrupted program and resume the original task.
  The status of the interrupted program should be noted in case of an interruption event. The information is then restored after the exception handler has completed its task. This will ensure that the processor can resume its original task correctly.

## Slide 6: Exception and Interruption
Interruption
  Refers to the exception caused by external events
  External event is also called interrupt request (IRQ).
  The exception handler here is also called interrupt service routine (ISR).
Thread
Mode
Exception
Mode
IRQ
Executing ISR
Executing normal code sequence
Finishing handler
Context saving
Context restoring
Notes: For example, interrupts can be generated using on-chip peripherals or by software. The majority of modern processors support both exceptions and interrupts. The software code that is executed when an interrupt occurs is called an interrupt handler or interrupt service routine (ISR). Both exception handlers and ISR are usually part of the program code in the compiled program image.

## Slide 7: Interrupt Preemption
The exceptions (or interrupts) are commonly divided into multiple levels of priorities.
  A higher priority exception can be triggered and serviced during a lower priority exception.
  Commonly known as a nested exception, or interrupt preemption
Main thread
Context switching
ISR
low priority
Main
ISR 1
Main
ISR 1
ISR2
Context switching
ISR
high priority
stacking
stacking
unstacking
unstacking
interrupt
interrupt
Notes: Exceptions can be divided into different levels of priority. This means that while an exception handler is running an exception of a low priority, a higher priority exception can be triggered and serviced. This is commonly known as a nested exception, as can be seen in this figure. The priority level of an exception can be manipulated or it can be a fixed value. Some exceptions can also be disabled or enabled by software.

## Slide 8: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: The Cortex-M0 processor, which is based on the Armv6-M architecture, contains a built-in interrupt controller that supports up to 32 interrupt request (IRQ) inputs and a non-maskable interrupt (NMI) input, as shown in this diagram.
The IRQ and the NMI can be generated from on-chip peripherals or external sources if the microcontroller design supports it. The nested vectored interrupt controller (NVICI) compares the priority between interrupt requests and the current priority level so that nested interrupts can be handled automatically. If an interrupt is accepted, the NVICI block communicates with the processor so that the processor can execute the correct interrupt handler. The NVIC block can accept a maximum of 32 interrupt request signals and an NMI input.

## Slide 9: Armv6-M Exception Model
Exception number | Exception type | Priority
1 | Reset | -3 (highest)
2 | NMI | -2
3 | HardFault | -1
4-10 | Reserved | 
11 | SVCall | Programmable
12-13 | Reserved | 
14 | PendSV | Programmable
15 | SysTick, optional | Programmable
16 + N | External interrupt 0-31 | Programmable
Notes: The Cortex-M0 supports an array of internal exceptions and each exception has a unique exception number. Exceptions generated inside the processor are given a number between 1 and 15 while external interrupts range from 16 to 47. Each of the exception types also have priority levels associated with them. These priority values can be fixed or programmable, as seen in the table. The table here shows a summary of exception types, exception numbers, and priority levels. We are now going to look at each of these types in more detail.

## Slide 10: Armv6-M Exception Model
Reset
  The Armv6-M profile supports two levels of reset.
  Power-on reset resets the processor, SCS, and debug logic.
  Local reset resets the processor and SCS, and not the debug-related resources.
  The reset exception is permanently enabled with a fixed priority of -3.
Non maskable interrupt (NMI)
  The second highest priority exception cannot be disabled.
  Useful for safety critical systems like industrial control or automotive
  Can be used for power failure handling or as a watchdog
Notes: This slide describes the Reset and NMI models. Note that the NMI is well designed for use in safety critical systems such as the automotive industry. Due to the fact that the NMI cannot be disabled by control registers, responsiveness is guaranteed.

## Slide 11: Armv6-M Exception Model
HardFault
  HardFault is the generic fault that exists for all classes of fault that cannot be handled by any of the other exception mechanisms.
  For example, trying to execute an unknown opcode, or a fault on a bus interface or memory system
SVCall (SuperVisor Call)
  SVCall exception takes place when SVC instruction is executed.
  Is usually used in an OS control
PendSV (Pendable Service Call)
  Similar to an SVCall, but does not immediately take place
  Starts only when high-priority tasks are completed
Notes: Three more models, HardFault, SVCall and PendSV, are described above.

## Slide 12: Armv6-M Exception Model
SysTick
  The System Tick timer is another feature of an OS application.
  Exception starts when an regular interrupt is generated from a timer.
External interrupts
  Supports up to 32 external interrupts, which can be connected from on-chip peripherals
  Needs to be enabled before being used
  Programmable priorities
Notes: With SysTick, regular interrupts are typically generated for system maintenance-related tasks such as context switching. The Cortex-M0 has an integrated timer. This makes it easier to port an OS from one device to another. The Cortex-M0 microcontroller could support anywhere from 1 to 32 interrupts. These interrupt signals can be internal or external. External interrupts should be enabled before being used, or the interrupt request will be stored in a pending status register. Interrupt request signals which can be accepted by the NVIC block can be either a high logic level or interrupt pulses. It should be noted here that external interrupt signals can be active high or active low, or they can have programmable configurations.

## Slide 13: Cortex-M0 Interrupt Controller
Memory map of nested vectored interrupt controller (NVIC)
Reserved
External Device
External RAM
Peripherals
SRAM
Code
Private Peripheral Bus
ROM Table
Reserved
System Control Space
(SCS)
Reserved
Break Point Unit
Data Watch Point Unit
Reserved
Debug Control
Nested Vectored
Interrupt Controller
(NVIC)
Reserved
SysTick Timer
Reserved
0xE000E000
0xE000EFFF
0xE0000000
0xE00FFFFF
0xE000E100
0xE000ED00
System Control Block
(SCB)
0xE000ECFF
0xE000ED8F
Notes: So far, we have looked at the types of exceptions supported by the Cortex-M0 processor. We have also seen that this processor has a built-in hardware unit called the nested vectored interrupt controller (NVIC), which provides the functionality for interrupt control and system exception support.
There are a maximum of 32 external interrupts and one non-maskable interrupt (NMI) that are supported in the Cortex-M0 architecture. Interrupt request signals that can be accepted by the NVIC block can either be high logic level or interrupt pulses. NVIC control registers can be used to independently enable or disable each external interrupt and its pending status. NVIC control registers can also be set or cleared manually; they are memory mapped and can be easily accessed in C language. The location of the NVIC registers starts from address 0xE000E100, as can be seen from this diagram.

## Slide 14: NVIC Registers
Address | Register
0xE000E100 | Interrupt set-enable register
0xE000E104 — 0xE000E17F | Reserved
0xE000E180 | Interrupt clear enable register
0xE000E184 — 0xE000E1FF | Reserved
0xE000E200 | Interrupt set-pending register
0xE000E204 — 0xE000E27F | Reserved
0xE000E280 | Interrupt clear-pending register
0xE000E300 — 0xE000E3FC | Reserved
0xE000E400 — 0xE000E41C | Interrupt priority registers
0xE000E420 — 0xE000E43C | Reserved
Notes: This table lists the addresses of the NVIC registers that can be used to enable and disable interrupt signals.

## Slide 15: NVIC Registers
Interrupt set-enable register
  Write “1” to enable one or more interrupts
  Write “0” has no effect
Interrupt clear enable register
  Write “1” to one or more interrupts
  Write “0” has no effect
Interrupt set-enable register
bit8
bit16
bit24
bit31
Write “1” to clear Interrupt #0
Interrupt clear enable register
Write “1” to enable Interrupt #0
Write “1” to enable Interrupt #31
0xE000E100
0xE000E180
Address
Notes: The NVIC registers are used in order to enable/disable the interrupt requests register. They can be accessed via two separate addresses. The 0xE000E100 address is used to enable an interrupt, while the 0xE000E180 address is used to disable an interrupt. The number of interrupt signals that can be supported depends on the width of the NVIC register, which can be up to 32 bits.

## Slide 16: NVIC Registers
Why use separate register addresses?
  Reduces the steps needed for enabling/disabling an interrupt, resulting in smaller code and less execution time
  Prevents the race condition; e.g., the main thread is accessing a register by “read-modify-write” process, and it is interrupted between its “read” and “write” operation. If the ISR again modifies the same register that is currently being accessed by the main thread, a conflict will occur.

## Slide 17: NVIC Registers
Interrupt pending and clear pending
  An interrupt goes into pending status if it cannot be processed immediately; e.g., a lower priority interrupt will be pending if a higher interrupt is being processed.
Notes: It is possible to access or modify the interrupt pending status through the interrupt set pending and interrupt clear pending register addresses shown previously. Like the interrupt enable control register, the interrupt pending status register is one register in a physical sense, but it uses two addresses in order to set and clear the bits. This helps prevent race conditions in the case of interrupt enable/disable registers.

## Slide 18: NVIC Registers
Interrupt priority registers
  The priority level configuration registers are eight bits wide, but only two bits are implemented in Cortex-M0.
  Since only two MSBs are used, four levels of priority can be represented: 0x00, 0x40, 0x80, and 0xC0.
bit3
bit2
bit1
bit0
bit7
bit6
bit5
bit4
Implemented
Not implemented
Reset
NMI
HardFault
Programmable
Exceptions
Possible priorities:
0x00, 0x40, 0x80, 0xC0
-3
-2
-1
0x40
0x80
0xC0
Highest priority
Lowest priority
0x00
Notes: The priority-level registers are used to determine the priority level of external interrupts.

## Slide 19: NVIC Registers
Interrupt priority registers
  Use eight 32-bit registers to set interrupt priorities for the 32 interrupts
  Each register contains the priority for four interrupts, and each interrupt priority is implemented using two bits.
0xE000E41C
bit8
bit16
bit24
bit32
0xE000E418
0xE000E414
0xE000E410
0xE000E40C
0xE000E408
0xE000E404
0xE000E400
bit1
27
31
30
29
28
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
24
25
26
Notes: There are eight 32-bit registers that are used to set interrupt priorities for the 32 interrupts. Each register contains the priority for four interrupts, and each interrupt priority is implemented using two bits. The unused bits are ignored and their read values return zeros. It is important to note here that those registers are only accessed using word-size transfer, so each access will affect four interrupt priority registers. Therefore, in order to change the contents of only one priority level register, its whole associated word must be read and only its corresponding byte is modified; then, the whole word is written back.

## Slide 20: Building a System on a Chip (SoC)
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-Segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral Drivers
AHB
Interrupt
Notes: Now that we understand the exception types in the Cortex-M0 and how to control external interrupts using the NVIC registers, we can start looking at how to design and implement an interrupt mechanism that responds to interrupts from the timer and UART.

## Slide 21: The Interrupt Mechanism Process
Implement interrupt generation mechanism in hardware
Connect interrupt signals to processor
Enable interrupts in software
Enter an exception handler
Exit from an exception handler
Notes: The process of implementing and executing an interrupt mechanism varies depending on the type of the interrupts and the ISR to be executed; however, there are common stages in the process, as follows:
Implement the interrupt generation mechanism in hardware
Connect interrupt signals to processor
Enable interrupts in software
Enter an exception handler
Exit from an exception
We will look in detail at each of these steps.

## Slide 22: Interrupt Implementation for Timer
Implement the interrupt mechanism for the AHB timer peripheral, for example:
  An interrupt is generated every time the counter reaches zero.
  A clear register needs to be added, which is used to clear the interrupt request once the processor finishes its ISR.
AHB
Interface
Data [31:0]
Addr [31:0]
Control [31:0]
addr
Address
Decoder
Data [31:0]
Load [31:0]
Current [31:0]
Clear [31:0]
32-bit
Counter
Clk
Prescaler
Counter
== 0?
Timer_irq
Interrupt request
Control [31:0]
Notes: To design our first interrupt mechanism, we use the timer peripheral we have implemented previously. We modify our initial design to add an interrupt signal generated every time the counter reaches zero. Such a signal will prompt the processor to execute an interrupt service routine. For example, displaying a number on the monitor or switching on one of the LEDs connected to the GPIO.

## Slide 23: Interrupt Implementation for UART
Implement the interrupt mechanism for the AHB UART peripheral
  For example, the interrupt can be generated if the receiver FIFO is not empty.
UART
Transmitter
UART
Receiver
Baud Rate
Generator
Transmitter
FIFO
Receiver
FIFO
UART TX
UART RX
Data
Start
Done
Tick
Tick
Ready
Data
Data
Done
Data
Ready
Full
8
8
8
8
Data [31:0]
Addr [31:0]
Control [31:0]
FIFO != empty?
Interrupt request
UART_irq
AHB
Interface
Notes: To design the second interrupt mechanism, we use the UART peripheral we implemented previously. We modify our initial design to add an interrupt signal if the receiver FIFO is not empty. Such a signal will prompt the processor to execute an interrupt service routine, for example, printing a character to the screen.

## Slide 24: Connect Interrupts to Processor
Connect the interrupts from peripherals to the Cortex-M0 microprocessor.
Note that in this set of teaching materials, we use a simplified version of Cortex-M0 (Cortex-M0 DesignStart), which only supports 16 external interrupts.
Arm Cortex-M0
Microprocessor
UART
Peripheral
Timer
Peripheral
UART_IRQ
timer_IRQ
Timer_IRQ
UART_IRQ
Processor_IRQ [15:0]
Processor_IRQ

## Slide 25: Enable Interrupts in Software
Configure NVIC:
  Set interrupt priority registers, for example:
  Set interrupt enable register, for example:
Make sure PRIMASK register is zero:
  Set to one will block all the interrupts, other than non-maskable interrupt (NMI) and the hard fault exception, for example:
LDR R0, =0xE000E400 : Address of priority0 register
LDR R1, [R0] : Get priority0 register
MOVS R2, #0xFF : Byte mask
BICS R1, R1, R2 : R1= R1 AND (Not (0x000000FF))
MOVS R2, #0x40 : Priority level
ORRS R1, R1, R2 : Update the value of priority register
STR R1, [R0] : Write back the priority register
LDR R0, =0xE000E100 : NVIC Enable register
MOVS R1, #0x1 : Interrupt #0
STR R1, [R0] : Enable interrupt #0
MOVS R0, #0x0 :
MSR PRIMASK, R0 : Clear PRIMASK register
Notes: In order to enable interrupts in the software, we first need to configure the NVIC registers. To do this, we need to specify the priority of each interrupt by setting the interrupt priority registers.
Then we need to enable the interrupt by setting the interrupt enable register. Some assembly code is shown here to illustrate how these two steps are performed.
After the NVIC registers are configured, we need to make sure that the PRIMASK register is set to zero, or it will block all interrupts apart from NMI and the hard fault exception. To achieve this, we can use the two instructions shown here.

## Slide 26: Entering an Exception Handler
Finish current instruction (except for lengthy instructions)
Look up the interrupt vector and branch to the entry address of the exception handler
Push context onto current stack (MSP or PSP)
Load PC with address of exception handler
Load LR with EXC_RETURN code
Load IPSR with exception number
Start executing code of exception handler
  Usually, there are 16 cycles from the exception request to execution of first instruction in the handler.
  The interrupt latency is the time delayed before entering an interrupt, which is an overhead that should be minimized.
Notes: Entering an exception handler is done as follows. First, finish the current instruction (except for lengthy instructions); then, look up the interrupt vector and branch to the entry address of the exception handler.
After that, push context onto the current stack (MSP or PSP). This process is called stacking, and occurs when an exception takes place. Eight registers are pushed to the stack automatically. These registers are R0 to R3, R12, R14 (the link register), the return address (address of the next instruction, or program counter), and the program status register (xPSR).
After stacking, load the PC with the address of the exception handler. Next, load LR with EXC_RETURN code; then, load IPSR with exception number. Finally, start executing the code of the exception handler.

## Slide 27: Exiting an Exception Handler
Clear the interrupt request of the peripheral, as follows:
  The timer can have a clear register, which is used to clear its interrupt request.
  Alternatively, the interrupt request can be automatically cleared by the peripheral itself under a certain condition; e.g., UART can clear its interrupt request after all data has been read out from its receiver FIFO.
Context restoring; pop up the registers from the stack.
Update IPSR
Load PC with the return address
Continue executing code of the previous program