## Slide 1: The Arm Cortex-M0 Processor Architecture: Part 2

## Slide 2: Module Syllabus
Basic Structure of Arm Thumb Instruction Set
Functionality of Cortex-M0 instructions, including:
  Data Accessing Instructions
  Arithmetic Instructions
  Logic Operations and Shift Instructions
  Program Flow Control and Exceptions-related Instructions
  Sleep Mode-related Instructions
  Main Power-saving Features of Cortex-M0

## Slide 3: Building a System on a Chip
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral drivers
AHB
Notes: To learn to program a processor at the assembly language level, which may be needed in the design process of an SoC, we need to understand its instruction set architecture. Put another way, we need to understand how the processor obtains information and manipulates data.
In this module, we will study the instruction set of a Cortex-M0 processor. We will also look at the main power saving features of this architecture.

## Slide 4: Thumb Instruction Set
Early Arm processors
  32-bit instruction set, called the Arm instructions
  Powerful and good performance
  Larger program memory compared to 8-bit and 16-bit processors
  Larger power consumption
Thumb-1 instruction set
  16-bit instruction set, first used in Arm7TDMI processor in 1995
  Provides a subset of the Arm instructions, giving better code density compared to 32-bit RISC architecture
  Code size is reduced by ~30%, but performance is also reduced by ~20%.
  Can be used together with Arm instructions using a multiplexer
Incoming
Instructions
Thumb Remap
to Arm
Arm
Instruction
Decoder
Instructions
Executing
T bit, 0: select Arm,
1: select Thumb
0
1
Notes: Arm instructions are 32-bit instruction sets that were used in early Arm processor designs. This set of instructions provides good performance and enhanced functionality. However, the main drawback of the Arm instruction set is that it requires larger program memory compared to 8-bit and 16-bit processors, and dissipates more energy.
The Thumb-1 instruction set is a 16-bit instruction set, first used in the Arm7TDMI processor in 1995. It provides a subset of the Arm instructions, with better code density in comparison to the 32-bit RISC architecture. Using Thumb-1 instructions means the code size can be reduced by around 30%, but performance is also reduced by about 20% compared to the original Arm instructions. One way to mitigate the reduced performance of the Thumb-1 instruction set is to use it together with Arm instructions, using a multiplexer as shown in this figure.

## Slide 5: Thumb-2 Instruction Set
Consists of both 32-bit Thumb and original 16-bit Thumb-1 instruction sets
Compared to the 32-bit Arm instruction set, code size is reduced by ~26%, while keeping a similar performance.
The Cortex-M0 processor uses a superset of 16-bit Thumb-1 instructions + minimum subset of 32-bit Thumb-2 instructions.
Notes: Thumb-2 technology consists of both 32-bit Thumb and original 16-bit Thumb-1 instruction sets. It was first introduced in 2003. Using Thumb-2 instructions, the code size can be reduced by around 26%, and performance remains the same compared to the 32-bit Arm instruction set. The Cortex-M0 processor uses a superset of 16-bit Thumb-1 instructions in addition to a minimum subset of 32-bit Thumb-2 instructions.

## Slide 6: Cortex-M0 Instruction Set
16-bit Thumb Instructions Supported on Cortex-M0 |  |  |  |  |  |  |  |  | 
ADCS | ADDS | ADR | ANDS | ASRS | B | BIC | BLX | BKPT | BX
CMN | CMP | CPS | EORS | LDM | LDR | LDRH | LDRSH | LDRB | LDRSB
LSLS | LSRS | MOV | MVN | MULS | NOP | ORRS | POP | PUSH | REV
REV16 | REVSH | ROR | RSB | SBCS | SEV | STM | STR | STRH | STRB
SUBS | SVC | SXTB | SXTH | TST | UXTB | UXTH | WFE | WFI | YIELD
32-bit Thumb-2 Instructions Supported on Cortex-M0 |  |  |  |  |  |  |  |  | 
BL | DSB | DMB | ISB | MRS | MSR |  |  |  | 
Note: some instructions have an “S” suffix, which is an updated Arm syntax used to support the Unified Assembler Language (UAL).
Notes: MRS and MSR are special register access instructions
ISB, DSB, and DMB are memory synchronization instructions
BL was supported in the traditional Thumb instruction set, but the bit field definition was extended in Thumb-2.

## Slide 7: Cortex-M0: Generic Format of Instructions
Two-operand format
  Mnemonic Operand1, Operand2
Three-operand format
  Mnemonic Operand1, Operand, Operand2
Notes: Before we start looking at the details of the Cortex-M0 instruction set, let us look at a typical instruction format we usually see in an assembly language program. The first field of the instruction is the “opcode,” which indicates the operation to be performed by the instruction, and it is usually three or four characters long. It should be noted that the same instruction may have two or three operands. So for a given operation such as a subtraction, we may see an instruction with two-operand format or three-operand format.
For a two-operand format, the destination register is also one of the operands. For example, if we were to use the ADD instruction with two operands, we add the destination register to the second operand and put the result back into the destination register. The first operand is in most cases a destination register that will be modified by the instruction. The last operand (Operand2), which is the second operand in a two-operand instruction or the third operand in a three-operand instruction, is considered a flexible operand. It can be used to specify another register or to provide a fixed constant. The second operand in the a three-instruction format is the source register, whose contents are accessed but not modified by the instruction.

## Slide 8: Cortex-M0 Instruction Set
Instruction Type | Instructions
Move | MOV, MOVS, MRS, MSR
Load/Store | LDR, LDRH, LDRB, LDRSH, LDRSB, LDM, LDMIA, STR, STRH, STRB, STMIA
Stack | PUSH, POP
Add, Subtract, Multiply | ADDS, ADCS, ADR, SUBS, SBCS, RSBS, MULS
Compare | CMP, CMN
Logical | ANDS, ORRS, EORS, MVNS, BICS, TST
Shift and Rotate | ASRS, LSRS, LSLS, RORS
Reverse | REV, REV16, REVSH
Extend | SXTB, SXTH, UXTB, UXTH
Conditional Branch | B, B <cond>, BL, BX, BLX
Memory Barrier | DMB, DSB, ISB
Exception | SVC, CPS
Sleep Mode | WFI, WFE, SEV
Other | NOP, BKPT, YIELD
Notes: A summary of the Cortex-M0 instruction set is shown in this table. We will study each of these instructions in detail.

## Slide 9: Cortex-M0 Instruction Set
Cortex-M0 Suffix
  Some instructions can be followed by suffixes to update processor flags or execute the instruction on a certain condition.
Suffix | Description | Example | Example explanation
S | Update APSR (flags) | ADDS R1, #0x21 | Add 0x21 to R1 and update APSR
EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE | Condition execution e.g., EQ= equal, NE= not equal, LT= less than | BNE label | Branch to the label if not equal

## Slide 10: Register Access: The Move Instruction
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
R0
0x00000001
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13
R14
R15
MOV R1 , #x01
Before execution After execution
Notes: Transferring data is one of the most common tasks in a processor. In Thumb code, the instruction mnemonic for moving data is MOV.
The first operand is the destination register, in this case, R1. The second operand is in this case a constant value; we call this immediate data, as it is readily provided within the instruction code.
The hash (#) symbol is often used to indicate that the operand is an immediate value. In order to indicate that a constant is written as a hexadecimal value, we need to add the prefix 0x.
If the first digit in a constant is a digit (1-9), the content will take a decimal value.
When this MOV instruction is executed, the value stored in R1 will be the full 32-bit value equivalent to the value specified.

## Slide 11: Memory Access: The LOAD Instruction
0X0000B04
LDR R5 , [R2]
0xAAAABBBB
0xAAAA0000
0xAAAA00CF
0x000000CF
0X0000B00
0X0000B04
0X0000B08
0X0000B0C
R0
R1
R2
R3
R4
R5
R6
0X0000B04
0xAAAA0000
R0
R1
R2
R3
R4
R5
R6
Before execution After execution
Notes: The MOV instruction can only access registers. It does not access memory. We access the memory using the LOAD/STORE instructions. The Cortex-M0 architecture is a load/store architecture, because most instructions do not access memory. For example, a MUL instruction cannot directly read a value from memory and multiply it with something. The result from a MUL instruction cannot be put directly into memory. To access memory either to get a value from a memory location or to store something in a memory location, we have to use the load and store instructions.
The load instruction uses a register as a pointer, so it gets the memory address from a register. It should be noted here that when a register (R2 in this case) is used as a pointer, its name is enclosed in square brackets when writing the instruction. In this example, the load instruction (LDR) uses the value stored in R2 as an address. It fetches what is stored in memory at that address and puts it into R5. So when this instruction is executed, the value in the specified memory location goes into R5.

## Slide 12: Memory Access: LOAD
Syntax | Description | Example | Example explanation
LDR <Rt>, =direct number | Load immediate data into a register. | LDR R0, =0x12345678 | R0= 0x12345678
LDR <Rt>, [<Rn>, constent] | Load word from memory Rt= memory [R1+4]. | LDR R0, [R1, 4] | R0= memory [R1+4]
LDR <Rt>, [<Rn>,<Rm>] | Load word from memory Rt= memory [<Rn>+<Rm>]. | LDR R0, [R1, R2] | R0= memory [R1+R2]
LDRH <Rt>, [<Rn>,<Rm>] | Load half word from memory Rt= memory [<Rn>+<Rm>]. | LDRH R0, [R1, R2] | R0= memory [R1+R2]
LDRB <Rt>, [<Rn>,<Rm>] | Load a byte from memory Rt= memory [<Rn>+<Rm>]. | LDRB R0, [R1, R2] | R0= memory [R1+R2]
Notes: The Cortex-M0 processor supports a number of load instructions, which support various data transfer sizes and addressing modes. The supported data transfer sizes are word, half-word, and byte. For these, we use LDR, LDRH, and LDRB, respectively.
It is possible using the load instruction to modify the address pointer. For example, the load instruction LDR R0, [R1, 4] uses offset addressing, which means a small fixed constant value is added to the value stored in the register (R1) and the result of this addition is used as the desired memory address.
So when the above instruction (LDR R0 [R1, 4]) is executed, the processor calculates the desired memory address is (R1 +4), and it fetches what is stored in memory at that address and puts it into register R0.

## Slide 13: Memory Access: LOAD
Syntax | Description | Example | Example explanation
LDRSH <Rt>, [<Rn>,<Rm>] | Load signed half word from memory Rt= SignExtend (memory [Rn+Rm]). | LDRSH R0, [R1, R2] | R0= memory [R1+R2]
LDRSB <Rt>, [<Rn>,<Rm>] | Load signed byte from memory Rt= SignExtend (memory [Rn+Rm]). | LDRSB R0, [R1, R2] | R0= memory [R1+R2]
Notes: Signed data types are commonly used in programming languages such as C, in which case, there is a need to sign extend the data. In the Cortex-M0 processor, sign extension is achieved using LDRSB and LDRSH instructions.

## Slide 14: Memory Access: The STORE Instruction
STR R5 , [R2]
0xAAAABBBB
0xAAAA0000
0xAAAA00CF
0x000000CF
0X0000B00
0X0000B04
0X0000B08
0X0000B0C
0X0000B04
0xBBBB000C
R0
R1
R2
R3
R4
R5
R6
0xAAAABBBB
0xBBBB000C
0xAAAA00CF
0x000000CF
0X0000B00
0X0000B04
0X0000B08
0X0000B0C
Before execution After execution
Notes: In order to copy a value from a register to a location in the memory space, we need to use the STORE instruction. The store instruction also uses a register to hold the desired memory address, similar to the LOAD instruction. However, the first operand of the store instruction is the source of the data value to be stored into memory. The second operand specifies the destination address in the memory.
The store instruction is one of the few instructions that use the first operand as the source and the second operand as the destination. When the processor executes the store instruction shown here, it copies the value stored in register 5 (the source) out to the memory address specified in register 1.

## Slide 15: Memory Access: STORE
Syntax | Description | Example | Example explanation
STR <Rt>, [<Rn>,<Rm>] | Write word to memory memory [<Rn>+<Rm>] = Rt. | STR R0, [R1, R2] | memory [R1+R2] = R0
STRH <Rt>, [<Rn>,<Rm>] | Write half word to memory memory [<Rn>+<Rm>] = Rt. | STRH R0, [R1, R2] | memory [R1+R2] = R0
STRB <Rt>, [<Rn>,<Rm>] | Write byte to memory memory [<Rn>+<Rm>] = Rt. | STRB R0, [R1, R2] | memory [R1+R2] = R0
Notes: The Cortex-M0 processor supports a number of store instructions, which support various data transfer sizes and addressing modes. The supported data transfer sizes are word, half-word, and byte, and for these, we use STR, STRH, and STRB, respectively.

## Slide 16: Multiple Data Access
Syntax | Description | Example | Example explanation
LDM <Rn>, {<Ra>, <Rb>, …} | Load multiple registers from memory. | LDM R0, {R1, R2 – R7} | R1= memory [R0], R2= memory [R0+4], … R2= memory [R0+24],
LDMIA <Rn>!, {<Ra>, <Rb>, …} | Load multiple registers from memory, and then increment Rn to the last address + 4. | LDMIA R0, {R1, R2 – R7} | R1= memory [R0], R2= memory [R0+4], … R0= R0 + 28
STMIA <Rn>!, {<Ra>, <Rb>, …} | Store multiple registers to memory, and then increment Rn to the last address + 4. | STMIA R0, {R1, R2 – R7} | memory [R0] = R1, memory [R0+4] = R2, … R0= R0 + 4×7
Notes: Multiple data access instructions allow loading or storing several registers simultaneously. For example, (LDM R0, {R1, R2–R7}) will load the registers R2, R3, R4, R5, R6, and R7 with the content stored in memory locations R0, R0+4,…R0+24. Another example is the LDMIA instruction, which performs a similar function to LDM. In addition, it increments the source register (Rn) to the last address plus 4. A third example is the STMIA instruction, which stores several registers into memory, and then increments Rn to the last address. It is important to note here that for load/store multiple instructions, the transfer size is always in word size.

## Slide 17: Stack Access: PUSH and POP
Syntax | Description | Example | Example explanation
PUSH {<Ra>, <Rb>, …} | Write single or multiple registers into memory and update base register. | PUSH { R0, R1, R2 } | Memory [SP- 4]= R0, Memory [SP- 8]= R1, Memory [SP- 12]= R2, SP = SP-12
POP {<Ra>, <Rb>, …} | Read single or multiple registers from memory and update base register. | POP { R0, R1, R2 } | R2 = Memory [SP], R1 = Memory [SP+ 4], R0 = Memory [SP+ 8], SP = SP+12
Notes: Access to stack memory can be achieved using PUSH and POP instructions. The PUSH instruction writes single or multiple registers into memory and updates the base register. The POP instruction reads single or multiple registers from memory and updates the base register.

## Slide 18: Arithmetic ADD
Syntax | Description | Example | Example explanation
ADDS <Rd>, <Rn>, <Rm> | Add two registers. Rd = Rn + Rm Update APSR. | ADDS R0, R1, R2 | R0 = R1 + R2 Update APSR.
ADDS <Rd>, <Rn>, #immed3 | Add an immediate constant into a register. Rd = Rn + ZeroExtend(#immed3), update APSR. | ADDS R0, R1, #0x01 | R0 = R1 + 0x01 Update APSR.
ADDS <Rd>, #immed8 | Add an immediate constant into a register. Rd = Rd + ZeroExtend(#immed8), update APSR. | ADDS R0, #0x01 | R0 = R0 + 0x01 Update APSR.
ADD <Rd>, <Rn> | Add two registers without updating APSR. Rd = Rd + Rm | ADD R0, R1 | R0 = R0 + R1
ADC <Rd>, <Rm> | Add with carry and update APSR. Rd = Rd + Rm + Carry Update APSR. | ADCS R0, R1 | R0 = R0 + R1 + Carry Update APSR.
ADD <Rd>, PC, #immed8 | Add an immediate constant with PC to a register without updating APSR. | ADD R0, PC, #0x04 | R0 = PC + 0x04
Notes: The add operation can be carried out between two registers, or between one register and an immediate constant. For example, the instruction:
ADDS R0, R1, R2
will add the values stored in R2 and R1 and store the results in R0. Because the Cortex-M0 uses a finite number of bits to represent numbers, arithmetic operation may sometimes lead to errors such as overflow; therefore, most of the arithmetic instructions will need to update the application program status register (APSR) in case of a fault as follows:
Set N flag to one if the result from ALU is negative.
Set the Z flag to one if the result from ALU is zero.
Set the C flag to one if an unsigned overflow occurs.
Set the V flag to one if a signed overflow occurs.
However, the (ADD <Rd>, PC, #immed8) instruction adds an immediate constant with PC to a register without updating APSR.

## Slide 19: Arithmetic SUB, MUL
Syntax | Description | Example | Example explanation
SUBS <Rd>, <Rn>, <Rm> | Subtract two registers. Rd = Rn - Rm Update APSR. | SUBS R0, R1, R2 | R0 = R1 - R2 Update APSR.
SUBS <Rd>, <Rn>, #immed3 | Subtract a register with an immediate constant. Rd = Rn - ZeroExtend(#immed3), update APSR. | SUBS R0, R1, #0x01 | R0 = R1 - 0x01 Update APSR.
SUBS <Rd>, #immed8 | Subtract a register with an immediate constant. Rd = Rd - ZeroExtend(#immed8), update APSR. | SUBS R0, #0x01 | R0 = R0 - 0x01 Update APSR.
SBCS <Rd>, <Rd>, <Rm> | Subtract with carry (borrow). Rd = Rd - Rm - Borrow Update APSR. | SBCS R0, R0, R1 | R0 = R0 - R1 - Borrow Update APSR.
RSBS <Rd>, <Rm>, #0 | Reverse subtract (negative). Rd = 0 - Rm, update APSR. | RSBS R0, R0, #0 | R0 = - R0
MULS <Rd>, <Rm>, <Rd> | Multiply two registers. Rd = Rd × Rm, update APSR. | MULS R0, R1, R0 | R0 = R0 × R1
Notes: The SUB and MUL instructions are very similar to the ADD instruction. These operations can be carried out between two registers, or between one register and an immediate constant.
All of the instructions shown in this slide will update (APSR) as follows:
Set N flag to one if the result from ALU is negative.
Set the Z flag to one if the result from ALU is zero.
Set the C flag to one if an unsigned overflow occurs.
Set the V flag to one if a signed overflow occurs.

## Slide 20: Arithmetic CMP
Syntax | Description | Example | Example explanation
CMP <Rn>, <Rm> | Compare two registers. Calculate Rn – Rm. Update APSR but subtract result is not stored. | CMP R0, R1 | Calculate R0-R1, Update APSR.
CMP <Rn>, #immed8 | Compare a register with an immediate constant. Calculate Rd – ZeroExtend (#immed8). Update APSR but subtract result is not stored. | CMP R0, #0x01 | Calculate R0-1, Update APSR.
CMN <Rn>, <Rm> | Compare negative. Calculate Rn – NEG(Rm). Update APSR but subtract result is not stored. | CMN R0, R1 | Calculate R0+R1, Update APSR.
Notes: The Cortex-M0 also supports a number of compare instructions that compare (using subtract) values and update flags (APSR), but the result of the comparison is not stored. For example, CMP R0, R1 calculates R0 – R1, and then updates APSR but the subtraction result is not stored. Another example, CMN R0, R1 calculates R0 – NEG (R1), and then updates APSR but the subtraction result is not stored; effectively, the operation is an ADD.

## Slide 21: Logic Operation
Syntax | Description | Example | Example explanation
ANDS <Rd>, <Rm> | Logical AND Rd = AND (Rd, Rm), update APSR | ANDS R0, R1 | AND (R0, R1), update APSR
ORRS <Rd>, <Rm> | Logical OR Rd = OR (Rd, Rm), update APSR | ORRS R0, R1 | OR (R0, R1), update APSR
EORS <Rd>, <Rm> | Logical exclusive OR Rd = XOR (Rd, Rm), update APSR | EORS R0, R1 | XOR (R0, R1), update APSR
MVNS <Rd>, <Rm> | Logical bitwise NOT Rd= NOT(Rm), update APSR | MVNS R0, R1 | R0 = NOT (R1), update APSR
BICS <Rd>, <Rm> | Logical bitwise clear Rd = AND (Rd, NOT(Rm)), update APSR | BICS R0, R1 | AND (R0, NOT(R1)), update APSR
TST <Rd>, <Rm> | Test (bitwise AND) Calculate AND (Rd, Rm), update APSR but the AND result is not stored | TST R0, R1 | Calculate AND (R0, R1), update APSR
Notes: The Cortex-M0 processor instruction set supports a variety of typical logic operations such as OR, AND, and so on. It also includes other types of logic operation such as TST instruction, which performs a bitwise AND. Logic operation instructions typically update the APSR.

## Slide 22: Arithmetic Shift Operation
Syntax | Description | Example | Example explanation
ASRS <Rd>, <Rm> | Arithmetic shift right Rd = Rd >> Rm, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | ASRS R0, R1 | R0 = R0 >> R1, update APSR
ASRS <Rd>, <Rm>, #immed5 | Rd = Rm >> immed5, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | ASRS R0, R1, #0x01 | R0 = R1 >> 1, update APSR
C
Register
Arithmetic shift right (ASR)
Notes: Shift and rotate instructions are also supported in the Cortex-M0, including both arithmetic shift operations and logical shift operations. In the case of arithmetic shift operations such as ASR instruction, the MSB is reserved when the data item is a signed integer value and the carry flag is updated using the last bit shifted out.

## Slide 23: Logical Shift Operation
Syntax | Description | Example | Example explanation
LSRS <Rd>, <Rm> | Logic shift right Rd = Rd >> Rm, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | LSRS R0, R1 | R0 = R0 >> R1, update APSR
LSRS <Rd>, <Rm>, #immed5 | Logic shift right Rd = Rm >> #immed5, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | LSRS R0, R1, #0x01 | R0 = R1 >> 1, update APSR
LSLS <Rd>, <Rm> | Logic shift left Rd = Rd << Rm, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | LSLS R0, R1 | R0 = R0 << R1, update APSR
LSLS <Rd>, <Rm>, #immed5 | Logic shift left Rd = Rm << #immed5, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | LSLS R0, R1, #0x01 | R0 = R1 << 1, update APSR
C
Register
Logic shift left (LSL)
0
C
Register
Logic shift right (LSR)
0
Notes: For logical shift operations, the instructions are LSLS and LSRS. For example, the instruction LSR R0, R1 will perform a logical right shift on the register R1 and store the results in the register R0. It will also update the N and Z flags in the APSR.

## Slide 24: Rotate Operation
Syntax | Description | Example | Example explanation
RORS <Rd>, <Rm> | Rotate right. Rd = Rd rotate right by Rm bits, last bit shift out is copy to APSR.C, APSR.N, APSR.Z are also updated | RORS R0, R1 | R0 = R0 >> R1 (rotate) Update APSR.
Rotate right (ROR)
C
Register
Notes: There is the only one rotate instruction, RORS. For example, RORS R0 R1 will rotate R0 right by R1 bits, it will also copy the last bit shifted to APSR.C. In addition, APSR.N and APSR.Z are updated.

## Slide 25: Reverse Ordering Operation
Syntax | Description | Example | Example explanation
REV <Rd>, <Rm> | Byte order reverse Rd = {Rm [7:0], Rm [15:8], Rm [23:16], Rm [31:24] } | REV R0, R1 | R0 = {R1 [7:0], R1 [15:8], R1 [23:16], R1 [31:24] }
REV16 <Rd>, <Rm> | Byte order reverse within half word Rd = {Rm [23:16], Rm [31:24], Rm [7:0], Rm [15:8] } | REV R0, R1 | R0 = {R1 [23:16], R1 [31:24], R1 [7:0], R1 [15:8] }
REVSH <Rd>, <Rm> | Byte order reverse within lower half word, then sign extend result Rd = SignExtend { Rm [7:0], Rm [15:8] } | REVSH R0, R1 | R0 = SignExtend { R1 [7:0], R1 [15:8] }
REV operation
Bit [7:0]
Bit [15:8]
Bit [23:16]
Bit [31:24]
Bit [7:0]
Bit [15:8]
Bit [23:16]
Bit [31:24]
REV16 operation
Bit [7:0]
Bit [15:8]
Bit [23:16]
Bit [31:24]
REVSH operation
Notes: The Cortex-M0 processor supports a number of instructions that can perform data reordering or extraction. These instructions are summarized in this table. For example, REV R0, R1, will reverse the order of the bytes stored in R1 and save the results in R0. The instruction performs byte order reverse within half word. REVSH performs byte order reverse within lower half word, then sign extends the result. These reverse instructions are usually used for converting data between little endian and big endian systems.

## Slide 26: Extend Operation
Syntax | Description | Example | Example explanation
SXTB <Rd>, <Rm> | SignExtend lowest byte in a word of data Rd = SignExtend ( Rm [7:0] ) | SXTB R0, R1 | R0 = SignExtend (R1 [7:0])
SXTH <Rd>, <Rm> | SignExtend lower half word in a word of data Rd = SignExtend ( Rm [15:0] ) | SXTH R0, R1 | R0 = SignExtend (R1 [15:0])
UXTB <Rd>, <Rm> | UnsignExtend lowest byte in a word of data Rd = ZeroExtend ( Rm [7:0] ) | UXTB R0, R1 | R0 = ZeroExtend (R1 [7:0])
UXTH <Rd>, <Rm> | UnsignExtend lower half word in a word of data Rd = ZeroExtend ( Rm [15:0] ) | UXTH R0, R1 | R0 = ZeroExtend (R1 [15:0])
Notes: The Cortex-M0 has a number of instructions to convert data between little endian and big endian systems. These are called “reverse instructions”. These are summarized in the above table. For example, the SXTB instruction extends a byte into a word using bit [7], while the UXTB instruction extends a byte to a word using zeros. Similarly, SXTH and UXTH can be used to extend a half word into a word.

## Slide 27: Program Flow Control
Syntax | Description | Example | Example explanation
B <label> | Branch to an address (unconditional) Branch range is +/- 2046 bytes of current PC. | B loop | Change PC to the address with label of “loop”.
B <cond> <label> | Conditional branch, branch to an address depending of APSR | BEQ loop | If APSR.Z =1, then change PC to the address with label of “loop”.
BL <label> | Branch and link, branch to an address and store return address to LR. Branch range is +/- 16MB of current PC. Usually used for calling a subroutine or function. Once the function is completed, it can be return by executing “BX LR” | BL functionA | Change PC to the address with label of “functionA,” LR = PC +4
BX <Rm> | Branch and exchange. Branch to an address specified by a register, and change processor state (Arm or Thumb) depending on bit[0] of the register (0 for Arm; 1 for Thumb) | BX R0 | PC = R0
BLX | Branch and link with exchange. Branch to an address specified by a register, save return address to LR, and change processor state depending on bit[0] of the register. | BLX R0 | PC = R0 LR = PC +4
Notes: The Cortex-M0 processor supports five control flow instructions, described above.

## Slide 28: Suffixes for Conditional Branch (B <cond>)
Suffix | Branch condition | Flags (APSR)
EQ | Equal | APSR.Z = 1
NE | Not equal | APSR.Z = 0
CS | Carry set | APSR.C = 1
CC | Carry clear | APSR.C = 0
MI | Negative | APSR.N = 1
PL | Positive | APSR.N = 0
VS | Overflow | APSR.V = 1
VC | No overflow | APSR.V = 0
HI | Unsigned higher | APSR.C = 1 and APSR.Z = 0
LS | Unsigned lower or same | APSR.C = 0 or APSR.Z = 1
GE | Signed greater than or equal | APSR.N = APSR.V
LT | Singed less than | APSR.N != APSR.V
GT | Signed greater than | (APSR.Z = 0) and (APSR.N = APSR.V )
LE | Signed less than or equal | (APSR.Z = 1) or (APSR.N != APSR.V)
Notes: The <cond> is one of the fourteen possible condition suffixes that are listed here.

## Slide 29: Conditional Branch Example
A simple loop
--------------------------------------------------------
MOVS R0, #4 ; Loop counter starting value is 4
loop ; “loop” is an address label
SUBS R0, #1 ; Decrement by 1 and update flag
BGT loop ; branch to loop if R0 is Greater Than (GT) 1
--------------------------------------------------------
Notes: The loop will execute four times. The fourth time, R0 is 1 before the SUBS instruction. After the SUBS instruction, the zero flag is set, so the condition for the branch failed and the program continues execution after the BGT instruction.

## Slide 30: Memory Barrier Instructions
Syntax | Description
DMB | Data memory barrier, Ensures that all memory accesses are completed before new memory access is committed
DSB | Data synchronization barrier, Ensures that all memory accesses are completed before the next instruction is executed
ISB | Instruction synchronization barrier, Flushes the pipeline and ensures that all previous instructions are completed before executing new instructions
Notes: Memory barrier instructions are used to manage access to the memory and avoid conflicts. They are typically needed in designs with complex memory architectures. The Cortex-M0 processor only has a simple single memory interface; therefore, the use of those instructions is rare. There are three memory barrier instructions that are supported on the Cortex-M0 processor: DMB, DSB, and ISB. Their uses are detailed in this table. It should be noted here that the operation of the Cortex-M0 is not going to be affected by omitting these instructions, which is not the case for other Arm processors.

## Slide 31: Exception-Related Instructions
Syntax | Description | Example | Example explanation
SVC <immed8> | Supervisor call Trigger the SVC exception. | SVC #3 | Trigger SVC exception, with parameter = 3
CPS | Change processor state. Enable or disable interrupt. Does not block NMI and hard fault handler | CPSIE I CPSID I | Enable interrupt (clearing PRIMASK) Disable interrupt (Setting PRIMASK)
Notes: We are going to look at two exception-related instructions.
The supervisor call (SVC) instruction causes the SVC exception to take place immediately if the exception priority level of SVC is higher than the current level. Typically, the SVC can be used to provide access to the system service or the application programming interface (API). An 8-bit immediate data element is used with SVC instruction to indicate which system service is required.
The CPS instruction is used to enable or disable interrupt by resetting or setting the PRIMASK special register.

## Slide 32: Other Instructions
Syntax | Description | Example | Example explanation
NOP | No operation Used to produce instruction alignment or to introduce delay | NOP | No operation
BKPT <immed8> | Breakpoint Put processor into halting stage, during which users carry out debug tasks through the debugger. Usually BKPT is inserted by a debugger to replace the original instruction. An 8-bit immediate data can be used as an identifier for the debugger. | BKPT #0 | Breakpoint, with identifier of 0
YIELD | Indicates task is stalled Used in multithread system, indicates that the current thread is delayed (e.g., waiting for hardware) and can be swapped out Executes as NOP on the Cortex-M0 processor | YIELD | Same as NOP in Cortex-M0 processor
Notes: Other instructions supported by the Cortex-M0 include:
The no-operation (NOP) instruction, which is used to produce instruction alignment or to introduce delay. This instruction takes one cycle minimum on the Cortex-M0. In general, delay timing produced by the NOP instruction is not guaranteed and can vary among different systems.
The breakpoint instruction is used to provide a breakpoint function during debug. When the breakpoint is hit, the processor would be halted, and the user can then carry out the debug tasks through the debugger. This instruction has an 8-bit immediate data field. This immediate value does not affect the breakpoint operation directly, but the debugger can extract this value and use it for debug operation.
The YIELD instruction is a hint instruction targeted at embedded OSs. This is not implemented in the current releases of the Cortex-M0 processor and executes as NOP.

## Slide 33: Sleep Mode Related Instructions
Syntax | Description
WFI | Wait for interrupt. Stops program execution until an interrupt arrives or until the processor enters a debug state
WFE | Wait for event. Stops the program execution until an event arrives (internal event register is set) or until the processor enters a debug state
SEV | Send event to all processors in multiprocessing environment (including itself).
Notes: There are a number of sleep mode-related instructions supported in the Cortex-M0 processor. These include:
The WFI instructions that halt execution until an exception arrives, apart from the case when it is masked by the exception mask registers or a debug entry request, if debug is enabled. There are other interrupts cases that cause the processor to wake up.
The WFE instruction has an almost identical functionality like WFI, except that it can also be awakened by events. An event can be an interrupt or the use of the SEV instruction as we will see later.
(Both WFI and WFE are intended for power saving only and can be treated as an NOP instruction.)
The SEV instruction causes an event to be signaled to all processors in a multiprocessor system. It also sets the local event register.

## Slide 34: Low-Power Requirements
The low-power requirements of systems vary but can be summarized as follows:
  Low operating power
  Low standby power
  High energy efficiency
  Wakeup latency
Notes: The low-power requirements of systems vary, but can be summarized as follows:
Low operating power: the power consumed during a normal operation of the system needs to be minimized. A significant portion of the operation’s power loss is caused by data transition activities.
Low standby power: the power consumed when the system is on standby mode needs to be minimized. A significant portion of the power loss while on standby is caused by leakage currents.
High energy efficiency: the number of operations that can be carried by a processor for each energy unit needs to be maximized. There are a number of metrics to estimate energy efficiency. For example, we could use a benchmark such as Dhrystone (DMIPS) and estimate the energy efficiency as of DMIPS/mW.
Wakeup latency: this is a measure of how long it will take the processor to exit the sleep mode.

## Slide 35: Cortex-M0 Low Power Features
Two architectural sleep modes:
  Normal sleep and deep sleep
Two instructions for entering sleep modes:
  WFE and WFI
Sleep-on-exit feature
  Allow processor to stay in sleep mode as much as possible.
Wakeup interrupt controller (WIC)
  An optional feature allows the clock of the processor to be completely removed during deep sleep.
Low-power design implementation
  Since the gate count is very low, the static leakage power is tiny compared to other 32-bit processors.
Notes: The Cortex-M0 processor is designed to target smaller embedded systems to meet ultra-low-power and high energy efficiency requirements.
The Cortex-M0 is a 32-bit processor, but only requires 12k gates, making it smaller than many 16-bit processors and much smaller than other 32-bit processors. Since the gate count is very low, the static leakage power is tiny compared to other 32-bit processors. On the other hand, the 32-bit architecture gives Cortex-M0 higher processing capability, which significantly reduces the operation duty cycle.
The Cortex-M0 is enhanced with two architectural sleep modes, which are supported by two instructions for entering sleep modes. The hardware architecture has an optional block called WIC. The latter allows the clock of the processor to be completely removed during deep sleep. This will save a great amount of dynamic power.

## Slide 36: Cortex-M0 Sleep Mode
The Cortex-M0 processor supports two sleep modes:
  Normal sleep: switch off some of the clock signals.
  Deep sleep: reduce voltage supplies to the memory blocks and switch off additional components.
To enter a sleep mode:
  Use WFE instruction.
  Use WFI instruction.
  Use the sleep-on-exit feature.

## Slide 37: Sleep-on-Exit Feature
The sleep-on-exit feature allows the processor to enter a sleep mode as soon as all the exception handlers are completed.
The power consumption is reduced since:
  The execution of unnecessary programs in the main thread is avoided.
  The unnecessary stacking and unstacking operation is avoided.
Main thread
WFI
Stacking
IRQ
ISR
Sleep
Sleep
Sleep-on-exit
(no unstacking)
Time
Priority
Notes: The sleep-on-exit feature is typically used in interrupt-driven applications as this maximizes the amount of time the processor can stay in sleep mode.

## Slide 38: How to Enable Sleep Features
The sleep features can be programmed by accessing the system control register (SCR) in the in the system control block (at address 0xE000ED10).
SCR
Bits | Field | Description
0 | Reserved | -
1 | SleepOnExit | Sleep-on-exit enable bit
2 | SleepDeep | Sleep mode type bit, 0: normal sleep; 1: deep sleep
3 | Reserved | -
4 | SeVOnPend | Send event on pend bit, enable generation of event by a new interrupt pending status
[31:5] | Reserved | -
SCR can be accessed by register symbol “SCB->SCR,” for example:
  SCB -> SCR = 1<1; //Enable sleep-on-exit bit
Notes: The sleep-on-exit feature is enabled by setting the bit[1]. To enable normal sleep mode we need to set bit[2] to zero. For deep sleep mode, we set the same bit to logic one. The Cortex-M0 also has a send-event-on-pend feature, which allows any interrupts (including disabled ones) to wake up the processor that stays in the sleep mode by executing the WFE instruction. This feature is controlled by bit[4] in the SCR register. When SEVONPEND bit is set, if an interrupt switches from inactive to pending state, an event will be generated, and the processor will be woken up from WFE sleep.

## Slide 39: Processor Wakeup Conditions
The processor can exit the sleep mode on different conditions.
Type | Priority | SeVOnPend | PRIMASK | Wake up | Execute ISR
WFE | IRQ priority > current level | -- | 0 | Yes | Yes
 | IRQ priority > current level | 0 | 1 | No | No
 | IRQ priority ≤ current level | 0 | -- | No | No
 | IRQ priority ≤ current level | 1 | -- | Yes | No
WFI | IRQ priority > current level | -- | 0 | Yes | Yes
 | IRQ priority > current level | -- | 1 | Yes | No
 | IRQ priority ≤ current level | -- | -- | No | No
Notes: The wakeup conditions after the execution of WFE or WFI instructions have both similarities and differences. Similarities include waking up on interrupt requests that are enabled and have a higher priority than the current level, and also the processor can be awakened by debug events.
One differences is that the execution of WFE does not enter sleep if the event register was set to 1, whereas execution of WFI always results in sleep. Also, a new pending disable interrupt can wake up the processor from WFE sleep if SEVONPEND is set. In addition, WFE can be awakened by an external event signal. This is not the case for WFI. And finally, WFI can be awakened by an enabled interrupt request when PRIMASK is set, which is different from the WFE instruction.

## Slide 40: Wakeup Interrupt Controller
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: The WIC is an optional unit, mainly used in low-power systems. In these applications, the processor can enter standby state while most of its parts are powered down.

## Slide 41: Wakeup Interrupt Controller
Usually requires a system-level power management unit (PMU)
When an interrupt is detected, the WIC sends a request to a PMU in the microcontroller to restore power and clock signals to the processor, and then the processor can wake up and process the interrupt request.
The WIC does not require extra programmable registers.
PMU
WIC
NVIC
Cortex-M0
IRQ & NMI
IRQ & NMI
Mask
Wake up
Power control
Deep sleep
Notes: The WIC block is used to decrease the power consumed by the processor. The WIC unit is only activated in deep sleep mode (i.e., when the SLEEPDEEP bit is set).

## Slide 42: Enter and Exit Deep Sleep Mode
Main thread
Mask WIC
WFI
(deep sleep)
Inform PMU
PMU put processor into low power state.
Deep sleep
IRQ
WIC detects, informs PMU
PMU put processor back to normal power.
ISR
WFI instruction is executed for deep sleep mode.
Processor sends mask information to WIC.
Processor informs PMU to put into low power state.
Processor deep sleep
IRQ occurs.
WIC first detects IRQ, and informs PMU to put power back to normal state.
WIC wakes up processor to start the ISR operation.

## Slide 43: Developing Low-Power Applications
Despite the low-power features of the processor, various things can reduce power consumption of an application:
  Run the processor at a suitable clock frequency.
  Disable a peripheral when not used.
  For interrupt-driven applications, the processor should stay in sleep mode as much as possible; e.g., use sleep-on-exit.
  Optimize the application code for speed to reduce active cycles (this may be at the cost of a larger code size).
  Turn off some of the clock signals or power supply when that piece of circuit is not used.