## Slide 1: The Arm Cortex-M0 Processor Architecture: Part 1

## Slide 2: Module Syllabus
Main Features of Arm Processor Families
The Cortex-M0 Arm Processor Architecture:
  Hardware Architecture
  Registers
  Memory Map
Notes: This module will review the processor architectures provided by Arm and explain in detail the inner structure and operation principles of the Cortex-M0 processor, one of the simplest architectures provided by Arm. It also covers the memory map of the Cortex-M0 and how exceptions are handled in this processor.

## Slide 3: Building a System on a Chip
Memory
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-segment
Peripheral
Arm CMSIS-Core
Application Programming Interface (API)
Application Design (e.g., Game)
Arm Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programming
Software high-level
application development
Peripheral Drivers
AHB
Notes: In this module, we will study the hardware architecture of the Cortex-M0, which will act as the core of our system.

## Slide 4: Arm Holdings
Designs Arm-based processors
Does not manufacture, but licenses designs to semiconductor partners who fabricate and sell to their customers
Also offers other designs, such as physical IPs, graphics cores, and development tools
Notes: Arm is an intellectual property (IP) provider. It designs and licenses a variety of processor architectures suitable for a wide range of SoC applications. Arm’s product portfolio also includes other designs such as physical IPs, graphics cores, and development tools. As a provider of IP cores, Arm does not manufacture but licenses designs to semiconductor partners who fabricate and sell to their customers. Therefore, the core business model of Arm is based on IP licensing.

## Slide 5: What Is Arm Architecture?
Arm architecture is a family of RISC-based processor architectures:
  Well-known for its power efficiency
  Hence, widely used in mobile devices, such as smartphones and tablets
  Designed and licensed to a wide ecosystem by Arm
Notes: Arm processor architectures are well known for their power efficiency; therefore, they are widely used in mobile devices such as smartphones and tablets.
What is more, the ecosystem surrounding Arm development gives Arm architecture a great advantage compared to proprietary architectures. Arm works with a variety of companies that provide software support for their devices such as OSs, compilers, and development tools.

## Slide 6: Example Design of an Arm-based SoC
1. Select a set of IP cores from Arm or other third-party IP vendors
2. Integrate IP cores into a single chip design
3. Give design to semiconductor foundries for chip fabrication
Arm-based
MCU Chip
ROM
Arm
Processor
RAM
System Bus
Peripherals
External Interface
SoC
SoC Design
Chip Manufacture
Licensable IPs
IP libraries
Cortex-A9
Cortex-R5
Cortex-M0
Arm7
Arm9
Arm11
AXI bus
AHB bus
APB bus
GPIO
I/O blocks
Timer
DRAM ctrl
FLASH ctrl
SRAM ctrl
Notes: The wide variety of IP cores provided by Arm greatly facilitates the design process of today’s complex SoCs; in fact, this process can be summarized in the three simple steps above.

## Slide 7: Arm Processor Families
Cortex-A series (advanced application)
  High-performance processors for open OSs
  Applications include smartphones, digital TV, server solutions, and home gateways.
Cortex-R series (real-time)
  Exceptional performance for real-time applications
  Applications include automotive braking systems and powertrains.
Cortex-M series (microcontroller)
  Cost-sensitive solutions for deterministic microcontroller applications
  Applications include microcontrollers, mixed signal devices, smart sensors, automotive body electronics, and airbags.
Cortex-A
SC000
SC100
SC300
Arm11
Arm9
Arm7
Cortex-R
Cortex-M
SecurCore
Classic
As of Nov 2017
Cortex-M7
Cortex-M4
Cortex-M3
Cortex-M1
Cortex-M0+
Cortex-M0
Cortex-M23
Cortex-M33
Cortex-R8
Cortex-R7
Cortex-R52
Cortex-R5
Cortex-R4
Cortex-A17
Cortex-A15
Cortex-A9
Cortex-A8
Cortex-A7
Cortex-A5
Cortex-A75
Cortex-A73
Cortex-A72
Cortex-A57
Cortex-A55
Cortex-A53
Cortex-A35
Cortex-A32
Notes: Arm’s product portfolio includes a range of processor families with different performance and power characteristics suitable for a variety of SoC applications.
The Cortex-A series includes a number of high-performance processors that can support open OSs. These processors are typically used in advanced embedded applications from smartphones, digital TV, set-top boxes, and rich IoT devices through to enterprise networking, and server solutions. The power efficiency of the Cortex-A processors can provide significant advantages in an increasingly energy-conscious application landscape.
The Cortex-R series includes processors with an exceptional performance for real-time applications where reliability, high availability, fault tolerance, maintainability, and deterministic real-time responses are essential. Application examples include automotive braking systems and powertrains.
The Cortex-M series is a range of scalable and compatible, energy-efficient, easy-to-use processors designed for cost-sensitive applications such as microcontrollers, mixed signal devices, smart sensors, automotive body electronics, and airbags.

## Slide 8: Arm Processor Families
SecurCore series
  High-security applications such as smartcards and e-government
Classic processors
  Include Arm7, Arm9, and Arm11 families
Cortex-A
SC000
SC100
SC300
Arm11
Arm9
Arm7
Cortex-R
Cortex-M
SecurCore
Classic
As of Nov 2017
Cortex-M7
Cortex-M4
Cortex-M3
Cortex-M1
Cortex-M0+
Cortex-M0
Cortex-M23
Cortex-M33
Cortex-R8
Cortex-R7
Cortex-R52
Cortex-R5
Cortex-R4
Cortex-A17
Cortex-A15
Cortex-A9
Cortex-A8
Cortex-A7
Cortex-A5
Cortex-A75
Cortex-A73
Cortex-A72
Cortex-A57
Cortex-A55
Cortex-A53
Cortex-A35
Cortex-A32
Notes: The SecurCore series provides powerful 32-bit security-enhanced solutions; these are used in a wide range of security applications such as e-Government smartcards, Pay TV, and banking.
Classic processors include Arm7, Arm9, and Arm11 families; these have been available for over 15 years, with the Arm7TDMI still the highest shipping 32-bit processor on the market, with over 1 billion devices shipping every quarter, or over 90 per second, and in excess of 500 licenses. This wide range of processors continues to be at the heart of over one quarter of all electronic products shipped today.

## Slide 9: Arm Cortex-M Series Family
The Cortex-M series includes Cortex-M0, M0+, M1, M3, M4 and M7.
Main features
  Energy-efficiency: Lower energy costs, longer battery life
  Smaller code: Lower silicon costs
  Ease of use: Faster software development and reuse
  Ideal for a variety of embedded applications such as smart metering, human interface devices, automotive and industrial control systems, white goods, consumer products, and medical instrumentation
Notes: In this course, we focus on the Cortex M-series family; however, all the SoC design techniques we are going to learn can also be applicable to other Arm processor families.
Cortex-M series processors have high performance efficiency (for example, the Cortex-M0 = 0.9 DMIPS/MHz) so they can get a task done in fewer cycles. Even a 32-bit multiply operation can be completed in one cycle). This means Cortex-M-based devices can spend more time in a low-power sleep state, offering better energy efficiency and longer battery life.
Smaller code: High code density is achieved using the Arm Thumb-2 instruction set, which allows the processor to use both 32- and 16-bit instructions.
Ease of use: The Cortex-M0 is designed as an ideal C target, with many modern compilers supporting it, and its interrupt service routines (ISRs) are able to be coded directly as C functions. This allows for faster software development and reuse.

## Slide 10: Arm Cortex-M Series Family
Processor | Arm Architecture | Core Architecture | Thumb® | Thumb®-2 | Hardware Multiply | Hardware Divide | Saturated Math | DSP Extensions | Floating Point
Cortex-M0 | Armv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M0+ | Armv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M1 | Armv6-M | Von Neumann | Most | Subset | 3 or 33 cycle | No | No | No | No
Cortex-M3 | Armv7-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | No | No
Cortex-M4 | Armv7E-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | Yes | Optional
Notes: The processors in the Cortex-M family share common features such as the use of the Thumb instruction set architecture. However, they also have a number of differences. For example, the Cortex-M0, M0+, and M1 are based on the Von Neumann processor architecture and do not have a floating point unit, whereas more recent designs such as the Cortex-M4 are based on Harvard architecture and do support a floating point unit. However, in general, all Cortex-M processors are designed for low power microcontroller applications.

## Slide 11: Cortex-M0 Processor
Cortex-M0
Smallest Arm processor
High code density
Lower power
Simplicity
Armv6-M architecture
Notes: The Cortex-M0 is the smallest Arm processor with an exceptionally small silicon area. The gate count is approximately 12k gates at minimum configuration.
  The use of the 16-bit Thumb instruction set allows for high code density. Additional powerful 32-bit Thumb-2 instructions allow all operations to be carried out in one CPU state.
The Cortex-M0 also offers low power consumption of around 16 µW/MHz for minimal configuration.
It is easy to use due to the small number of instructions (56) and the fact that it can be programmed using C. Its response time is more deterministic, which means its performance is predictable and not subject to variations.
It uses the Armv6-M architecture, which we will look at later.

## Slide 12: Arm Processor v Arm Architectures
An Arm architecture:
  Describes the details of data storage structures (registers, memories)
  Explains the architectures of the instruction sets and programmer’s model
  Outlines how the processor handles exceptions
  This is all documented in the Arm v6-M Architecture Reference Manual
Notes: In order to understand the operation principles of the Arm architecture, we first need to know where processors store or obtain information from. Probably the most important of those will be the registers that are used for short-term memory, which will be located close to the processor’s ALU and are designed to be fast at the expense of power and transistors.
In addition, we should consider two main types of memory. The flash memory is where the program software is stored, which is non-volatile, so its contents are preserved even if the power is turned off and they are immediately available when the power is turned on. The second type of memory is called RAM; most of the variables used by the program will be stored in RAM. The content of RAM will be undefined when the power is turned on. It is worth noting here that the Cortex-M0 architecture treats the IO devices as another type of memory.
We also need to know how the processor manipulates data, so we must understand the detailed architecture of the instruction set. The processors in the Cortex-M family can’t execute programs written in a high-level language like C or Java directly; each statement in the programs must be converted into a sequence of assembly language instructions. The latter are the native programming language of the particular processor. The assembly language instructions of a particular processor depend on the processor hardware architecture. Understanding the processor assembly language gives the programmer a model of the processor architecture. Although most of the codes for embedded applications are written in a high-level language, most embedded projects require some code to be written in assembly language.
In addition, we need to understand how the processor handles exceptions. Exceptions are events that cause the program flow to exit the current program thread, and execute a piece of code associated with the event. For example, if the processor has to respond to a fault condition, then the processor will take control of the program execution and do something special to resolve the issue. We should note here that events can be either internal (e.g., fault conditions) or external (urgent requests from external pins).

## Slide 13: Arm Processor v Arm Architectures
Arm processors
  Are developed using one of the Arm architectures
  Contain more implementation-related information
  This is all documented in the processor’s technical reference manual.
  Example: Cortex-M0: v6-M
As of Sept 2013
Arm v6-M
Architecture
Arm v6
Architecture
Arm v7-M
Architecture
Arm
Cortex-M0
Thumb instruction set
Memory map
exception model
Thumb-2 system
Low power optimized
design
Notes: It is worth noting here the difference between an Arm architecture and an Arm processor. The processor is developed based on a specific architecture that includes memory map, registers, instruction set architecture, and exception model. In addition, the processor includes more implementation details such as timing information and hardware structures.
For example: The Cortex-M0 is developed based on the Arm v6-M architecture, which is a combination of Armv6 architecture’s Thumb instruction set and Armv7-M architecture memory map, exception model, and Thumb-2 system. The hardware design of the Cortex-M0 is optimized for low power.

## Slide 14: Cortex-M0 Overview
32-bit reduced instruction set computing (RISC) processor
Von Neumann architecture
  Both data and instructions share a single bus interface.
Instruction set
  56 instructions as a subset of Thumb-1 (16-bit) and Thumb-2 (16/32-bit)
Load-store architecture
Supported interrupts
  Non-maskable interrupt (NMI) + 1 to 32 physical interrupts
Supports sleep modes
Notes: The Cortex-M0 processor uses 16-bit Thumb instructions, which allows for high code density. In addition, several newer instructions from the Armv6 architecture and a few instructions from the Thumb-2 technology are also included. Thumb-2 technology has extended the previous Thumb instruction set to allow all operations to be carried out in one CPU state. Most instructions generated by the C compiler use the 16-bit instructions, and the 32-bit instructions are used when the 16-bit version cannot carry out the required operations. This results in high code density and avoids the overhead of switching between two instruction sets.
In total, the Cortex-M0 processor supports only 56 base instructions.
The Cortex-M0 processor is classified as a load-store architecture. To process data in the memory, it has to be loaded from memory to a register, processed inside the processor, and then written back to the memory if needed.

## Slide 15: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: A simplified block diagram of the Cortex-M0 is shown in this slide.

## Slide 16: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: The processor core is designed based on a three-stage pipeline; namely, fetch, decode, and execution. It includes an ALU and 16 32-bit register banks, data path, and control logic.

## Slide 17: Cortex-M0 Three-stage Pipeline
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Instruction 1
Instruction 2
Instruction 3
Fetch
Decode
Execute
Instruction 4
Time
Notes: This diagram illustrates the operation principles of a three-stage pipeline. The essence of this architecture is that it allows up to three instructions to be handled concurrently. For example, when the first instruction is being executed, the processor can decode the second instruction and fetch the third instruction at the same time, this helps enhance the throughput of the processor’s pipeline, resulting in better performance.

## Slide 18: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: The NVIC compares the priority between interrupt requests and the current priority level so that nested interrupts can be handled automatically. If an interrupt is accepted, the NVIC block communicates with the processor so that the processor can execute the correct interrupt handler.
The NVIC block can accept up to 32 interrupt request signals and an NMI input.

## Slide 19: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: When designing low power systems, the WIC is typically included in the Arm Cortex-M0 architecture. The use of WIC typically requires a system-level power management unit (PMU). The WIC block masks interrupt signals while the processor is in sleep mode. When an interrupt is detected, the WIC sends a request to the PMU to restore power and clock signals to the processor, and then the processor can wake up and process the interrupt request. The WIC does not require extra programmable registers. The WIC unit is activated only in deep sleep mode.

## Slide 20: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: The internal bus system, the data path in the processor core, and the AHB-Lite bus interface are all 32 bits wide.
The bus interface is based on AHB-Lite. This is an on-chip bus protocol used in many Arm processors. This protocol is part of the advanced microcontroller bus architecture (AMBA) specification, a bus architecture developed by Arm that is widely used in the IC design industry.

## Slide 21: Cortex-M0 Block Diagram
Internal Bus System
AHB-Lite
Bus Interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
Arm Cortex-M0 Microprocessor
Memory and Peripherals
JTAG/Serial-Wire
Debug Interface
Power Management Interface
Notes: The debug subsystem provides a standard debugging interface. The processor is suspended when a debug event takes place and the debug subsystem block allows the execution of one instruction at a time in order to observe how the registers and memory change or to run the processor at full speed until a particular instruction is executed.

## Slide 22: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: Let us now look at the registers in a Cortex-M0 processor; this architecture has sixteen 32-bit generic registers. In general, any of these registers can be used as an operand of an assembly language instruction that needs a register operand.

## Slide 23: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: However, only thirteen of these registers are intended for general purposes, namely, R0–R12. They can hold data or an address. It is important to know that registers do not know whether they hold data or an address and it is up to the programmer to keep track of that.
In the basic definition of the Cortex-M0 processor, there are three data types: byte of 8 bits, half word of 16 bits, or word of 32 bits.
The low registers (R0–R7) can be accessed by any instruction, but the high registers (R8–R12) sometimes cannot be accessed by some Thumb instructions.

## Slide 24: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes:   Three of the registers have special purposes; R13 is the SP. You may know that the stack is a very important data structure and is dynamically allocated in RAM memory. The SP keeps track of the memory’s address that holds the last value stored on the stack. It is used for saving the context of a program while switching between tasks. Many processors do not treat the SP as a generic register, but doing so makes it very easy to access data on the stack as we will see later.
There are two SPs in the Cortex-M0 processor, namely, main (MSP) and process (PSP). For simple applications the MSP is typically used all the time. For applications that require privileged access, we may need to use both: the MSP for OS kernel and exception handlers and the PSP for other tasks.

## Slide 25: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: R14 is the PC and is usually maintained directly by the processor hardware. It contains the address of the next assembly instruction that will be executed.
  The PC is automatically incremented by 4 at each operation (for 32-bit instruction code), except branching operations.
The PC is sometimes used as a pointer to access constants used by the code.
The PC can be accessed by the Arm assembler using either “R15” or “PC,” in either upper or lower case.

## Slide 26: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: R14 is the LR. Whenever you call a subroutine in the Cortex-M0 architecture, the LR is automatically loaded with the return address, so at the end of the subroutine, we use the value on the LR to get back to the calling program.

## Slide 27: Cortex-M0 LR
R14: LR
  The LR is used to store the return address of a subroutine or a function call.
  The PC will load the value from the LR after a function is finished.
PC
LR
Main
program
code
Subroutine
Current PC
Load PC with the address in LR to return to the main program
Current LR
Return from a subroutine to the main program
PC
LR
Main
program
code
Subroutine
Current PC
1. Save current
PC to LR
2. Load PC with the starting address of the subroutine
Call a subroutine
Code region
Code region
Notes:   This diagram illustrates how we can use the LR in a branching operation, such as function calls.
  First, we save the current PC to the LR; then, we load the PC with the starting address of the subroutine. At the end of the subroutine, we load the PC with the address in the LR to return to the main program.

## Slide 28: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: The combined PSR provides information about program execution and the ALU flags. It consists of the following three PSRs:
Application PSR (APSR)
Interrupt PSR (IPSR)
Execution PSR (EPSR)

## Slide 29: Cortex-M0 PSRs
xPSR, combined PSR
  Provides the information about program execution and the ALU flags
  Application PSR (APSR)
  Interrupt PSR (IPSR)
  Execution PSR (EPSR)
N
Z
C
V
ISR number
Reserved
Reserved
Reserved
T
Reserved
T
N
Z
C
V
ISR number
APSR
IPSR
EPSR
xPSR
bit0
bit8
bit16
bit24
bit31
Notes: APSR, IPSR, and EPSR registers provide the information about program execution and the ALU flags. They can be accessed as individual registers, a combination of any two from three, or a combination of all three using the MRS and MSR instructions. The APSR contains the condition code flags (N, Z, C, and V). Before entering an exception, the processor saves the condition code flags on the stack. The IPSR contains the ISR number of the current exception activation. The EPSR contains the Thumb state bit (T-bit). This bit is normally set to 1 for the Cortex-M0, because it only supports the Thumb state.

## Slide 30: Cortex-M0 Registers
APSR
  N: negative flag
  Set to one if the result from ALU is negative
  Z: zero flag
  Set to one if the result from ALU is zero
  C: carry flag
  Set to one if an unsigned overflow occurs
  V: overflow flag
  Set to one if a signed overflow occurs
IPSR
  ISR number
  Current executing ISR number
EPSR
  T: Thumb state
  Always one since Cortex-M0 only supports the Thumb state
Notes: Here is a summary of the three PSRs and their uses.

## Slide 31: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: Another special register is the PRIMASK register.

## Slide 32: Cortex-M0 Registers
PRIMASK: Interrupt mask special register
  1-bit PRIMASK
  Setting it to one will block all the interrupts apart from NMI and the hard fault exception.
Reserved
PRIMASK
PRIMASK
bit0
bit31
Notes: The PRIMASK register is a 1-bit-wide interrupt mask register. When set, it blocks all interrupts apart from the NMI and the hard fault exception. Effectively, it raises the current interrupt priority level to 0, which is the highest value for a programmable exception. The PRIMASK register can be accessed using special register access instructions (MSR and MRS) as well as using an instruction called the change processor state (CPS). This is commonly used for handling time-critical routines.

## Slide 33: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt Mask Register
Stack Definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General Purpose
Register
Notes: The last special register is the CONTROL register.

## Slide 34: Cortex-M0 Registers
CONTROL: Special register
  1-bit stack definition
  Set to one: use the PSP.
  Clear to zero: use the MSP.
Reserved
CONTROL
bit31
Stack definition
Reserved
Notes: As explained previously, there are two SPs in the Cortex-M0 processor. The SP selection is determined by the processor mode as well as the configuration of the CONTROL register in this figure. After reset, the MSP is used but can be switched to the PSP by setting bit [1] in the CONTROL register.
On a final note, bit 0 of the CONTROL register is reserved to maintain compatibility with the Cortex-M3 processor. In the Cortex-M3 processor, bit 0 can be used to switch the processor to user mode (non-privileged mode). This feature is not available in the Cortex-M0 processor.

## Slide 35: Cortex-M0 Memory Map
Private peripherals
e.g., NVIC, SCS
Mainly used for external peripherals
e.g., SD card
Mainly used for external memories
e.g., external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g., AHB, APB peripherals
Mainly used for data memory
e.g., on-chip SRAM, SDRAM
Mainly used for program code
e.g., on-chip FLASH
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
ROM Table
Reserved
System Control Space
(SCS)
Reserved
Break Point Unit
Data Watch Point Unit
Reserved
Debug Control
Nested Vectored
Interrupt Controller
(NVIC)
Reserved
SysTick Timer
Reserved
System Control Block
(SCB)
Notes: The Cortex-M0 processor has a full 32-bit address that requires 4 GB (4*2exp30) of memory space. So memory addresses in this processor will range from 0x00000000 to 0xffffffff.
The basic data types stored in the memory can be a byte of 8 bits, half word of 16 bits, or word of 32 bits, and that is really all the processor knows. It does not know what the data means; it is up to the programmer to keep track of that. Because the processor allows data values that are bytes, memory addresses are stored as byte addresses so a particular memory address specifies a particular byte in memory. So we need to access an entire word in memory to get it; the processor begins at the specified byte address and then also accesses the next three byte addresses to get a full 32-bit word.
You also need to know that there are predefined regions within the memory map as specified by Arm and those regions have different distinct characteristics. Each region is given for recommended usage.
Nevertheless, despite the default memory map, the actual usage of the memory map can also be flexibly defined by the user, except some fixed memory addresses, such as internal private peripheral bus.

## Slide 36: Cortex-M0 Executable Memory Space
Code region
  Primarily used to store program code
  Can also be used for data memory and on-chip memory, such as on-chip FLASH
SRAM region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
External RAM region
  Primarily used to store large data blocks, or memory caches
  Off-chip memory, slower than on-chip SRAM region
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Notes: There are predefined regions within the memory map as specified by Arm and those regions have distinct characteristics. For example, some of the regions highlighted in red are considered to be executable, so you can execute instructions in that address space. If you try to execute an instruction that is not in the executable memory space, it will cause a fault.
The code region is primarily used to store program code, but can also be used for data memory and on-chip memory, such as on-chip FLASH.
The SRAM region is primarily used to store data, such as heaps and stacks, but it can also be used for program code. Despite its name “SRAM,” the actual device could be SRAM, SDRAM, or other types.
The external RAM region is used for various purposes, such as data storage and memory caches.

## Slide 37: Cortex-M0 Device Memory Space
Peripheral region
  Primarily used for peripherals, such as advanced high-performance bus (AHB) or advanced peripheral bus (APB) peripherals
  On-chip peripherals
External device region
  Primarily used to map to external devices
  Off-chip devices, such as secure digital (SD) cards
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Notes: Some of the spaces are considered to be device spaces, which means that access to different addresses in those spaces have to occur in the same sequence that is specified in the code. These include the peripheral region that is primarily used for peripherals such as AHB or APB peripherals and for on-chip peripherals, and the external device region that is mainly used to map to external devices. It is for off-chip devices, such as SD cards.

## Slide 38: Cortex-M0 Private Peripheral Bus
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xE0000000
Private Peripheral Bus
0xE00FFFFF
ROM Table
Reserved
System Control Space
(SCS)
Reserved
Break Point Unit
Data Watch Point Unit
Reserved
Debug Control
Nested Vectored
Interrupt Controller
(NVIC)
Reserved
SysTick Timer
Reserved
System Control Block
(SCB)
Notes: The registers that control peripherals that are a mandatory part of the Cortex-M architectures are mapped here. For example, the NVIC is a standard interrupt controller for all Cortex-M processors. Therefore, there is a standard definition of the register that controls it. The system tick timer is used to control the flow of multitasking in real-time Oss; it is a standard part of the Cortex-M architecture and it is controlled by registers in this space. A system for fault status and control exists here, if we do things like divide by zero.

## Slide 39: Cortex-M0 Reserved Memory Space
Reserved region
  It is 512 MB at the top of the memory.
  Its content is vendor specific.
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000

## Slide 40: Cortex-M0 Memory Map Example
AHB Bus
External SRAM,
FLASH
External LCD
SD card
Cortex-M0
PPB
SCS
NVIC
Debug Ctrl
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External Memory Interface
(External RAM Region)
External Device Interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon
Notes: Although the Cortex-M0 processor has a fixed memory map, memory usage is very flexible. For example, it can have multiple SRAM memory blocks placed in the SRAM region as well as the CODE region, and it can execute program code from external memory components located in the RAM region. Device vendors can also add their own system-level memory features, such as system-level cache, if needed.
For a typical system developed with the Cortex-M0 processor, you can usually find the following elements as shown in this figure:
Flash memory (for program code)
Internal SRAM (for data)
Internal peripherals
External memory interface (for external memories as well as external peripherals (optional))
Interfaces for other external peripherals (optional)
For many low-cost applications, the system designs do not have any external memory interface or SD card interface. In these cases, some of the memory regions, like the external RAM or the external device regions, might not be used.

## Slide 41: Cortex-M0 Endianness
Endian refers to the order of bytes stored in the memory.
  Little endian: lowest byte of a word-size data is stored in the bit 0 to bit 7.
  Big endian: lowest byte of a word-size data is stored in the bit 24 to bit 31.
  Cortex-M0 supports both little endian and big endian.
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory
Notes: Endian refers to the order of bytes stored in the memory.
Little endian: lowest byte of a word-size data is stored in the bit 0 to bit 7.
Big endian: lowest byte of a word-size data is stored in the bit 24 to bit 31.
The Cortex-M0 processor supports either the little endian or big endian memory format. The microcontroller vendor makes the choice when the system is designed. Software developers must configure their development tools project options to match the endianness of the targeted microcontroller.
Cortex-M0 supports both little endian and big endian.